Alternator math– chapman
Q. Need of insulation at the armature coil for generating high voltage using alternator?
# 16 series
## 1
a)
Fleming's right-hand rule (for generators) shows the direction of induced current when a conductor attached to a circuit moves in a magnetic field. It can be used to determine the direction of current in a generator's winding.
Fleming’s Right Hand Rule states that if we arrange our thumb, forefinger and middle finger of the right-hand perpendicular to each other, then the thumb points towards the direction of the motion of the conductor relative to the magnetic field, the forefinger points towards the direction of the magnetic field and the middle finger points towards the direction of the induced current.
E=Blvsin(theta)
b) Dynamo is an older term of DC generator. Difference between generated voltage and terminal voltage is because of the armature drop.
c) math -khuje pai nai.
d) brush position at dynamo
## 2
a)
b) failure of the generator to build up
- No residual magnetism
- Field connection reversed
- Field resistance too high
- Open field connection
- Dirty commutator
c) – math pari na.
d) external characteristic curve of self excited DC generator.

## 3.
a) math korar moto enough info nai. May be explanation dite hbe je kon generator koto power supply dibe.
b) Significance of counter emf?
li­nk
Significance Of Back EMF
Back EMF +regulates the armature current and, as a result the armature current automatically maintains the load requirement. Let us understand how the Back EMF regulates the armature current.

How Back EMF regulates the flow of armature current?

Case 1: When the applied armature voltage is increased
The back EMF limits the armature current and make the motor self regulating. If the applied voltage is increased the armature current increase momentarily and the speed of the motor increase. The increased speed of the motor increases the back EMF and the armature current gets reduced.

Case 2: When the speed of DC motor gets decreased
Eb= (V-IaRa)
Ia= (V-Eb)/Ra
If the speed of the motor gets decreased because of the increased loading, the driving torque becomes less than the load torque and motor slow down and the back EMF gets decreased.The decreased back EMF will allow the more armature current to flow in the armature winding.The increased armature current will produce more torque which will produce the torque required by the load.When the motor attains the normal speed the back EMF will get reduced and thus the armature current get reduced. Thus the self regulation of the armature current is achieved.
Case 3: When the speed of DC motor gets increased
If the load on the motor is decreased, the driving torque becomes more than the load torque and, the motor speed increases and the increased speed cause increase in the back EMF. The increased back EMF opposes the applied DC voltage and thus the armature current gets decreased.The motor stops accelerating and the speed again bring back to the point that meets the exact load requirement.
Thus the back EMF regulates the armature current according to the load requirement.
## 4 ( pura 3 point, 4 point starter pora lagbe)
a) Disadvantage of 3 point starter? How a 4 point starter can remove this disadvantage?
b) methods of breaking(DC motor). Regenerative breaking?
c) math - resistance of each step of a starter
## 5
a) DC generator produces AC voltage. How?
b) advantages of stationary armature over rotating armature?
Ans:
- Due to the simple and robust construction of the rotor, the higher speed of rotating DC field is possible. This increases the output obtainable from a machine of given dimensions.
- It is easier to insulate stationary winding for high voltages for which the alternators are usually designed. It is because they are not subjected to centrifugal forces and also extra space is available due to the stationary arrangement of the armature.
- The stationary 3-phase armature can be directly connected to load without going through large, unreliable slip rings and brushes.
- Only two slip rings are required for d.c. supply to the field winding on the rotor. Since the exciting current is small, the slip rings and brush gear required are of light construction.

c) synchronous impedance?
The synchronous impedance may be defined as the vector sum of the armature resistance and synchronous reactance. It is denoted as Zs.
d) math- korsi. Phasor diagram aki nai.
## 6
a) effect of change of load on an alternator for lagging and leading
pf and unity pf?
b) how does a synchronous motor operate? How to make it self
starting?
Ans:
In this method, the motor is first started as an induction motor and then starts running as a synchronous motor after achieving synchronous speed. For this, damper windings are used. Damper windings are additional windings consisting of copper bars placed in the slots in the pole faces. The ends of the copper bars are short-circuited. These windings behave as the rotor of an induction motor. When 3 phase power is supplied to the motor, the motor starts running as an induction motor at a speed below synchronous speed. After some time DC supply is given to the rotor. The motor gets pulled into synchronism after some instant and starts running as a synchronous motor. When the motor reaches synchronous speed, there is no induced emf in the damper windings anymore and hence they don’t have any effect now on the working of the motor. This is the most commonly used technique for starting synchronous motors.
c) math
## 7
a) synchronous condenser, slipping a pole, speed regulation, slip?
a synchronous condenser is a DC-excited synchronous motor, whose shaft is not connected to anything but spins freely.
Pole slipping typically occurs under severe fault conditions which cause a transient torque on the generator which exceeds the ability of the field to hold the generator rotor synchronized to the stator.
The speed regulation of a motor is defined as the change in the speed from full-load to no-load and is expressed as a percentage of the full-load speed.
In an induction motor, slip is a measure of the difference between the machine's synchronous speed and its shaft speed.
b) method of starting a poly phase synchronous motor?
c) math
## 8
a) servo motor? Def, application
A servo motor is a motor that allows for a precise control in terms of the angular position, acceleration, and velocity.
Application:
- Cameras, telescopes and antennas for adjusting the focus
- Elevator technology
- Robotics (on joints)
- Industrial production
b) operation of stepper motor-explain
The stepper motor working principle is Electro-Magnetism. It includes a rotor which is made with a permanent magnet whereas a stator is with electromagnets. Once the supply is provided to the winding of the stator then the magnetic field will be developed within the stator. Now rotor in the motor will start to move with the rotating magnetic field of the stator. So this is the fundamental working principle of this motor.
In this motor, there is a soft iron that is enclosed through the electromagnetic stators. The poles of the stator as well as the rotor don’t depend on the kind of stepper. Once the stators of this motor are energized then the rotor will rotate to line up itself with the stator otherwise turns to have the least gap through the stator. In this way, the stators are activated in a series to revolve the stepper motor.
c) universal motor related question. (out of our pora)